## Slide 1: SOCKET COMMUNICATION USING C42QM
ALISHA BENNY

## Slide 2
This study focuses on understanding how TCP socket communication works in Cavli IoT modules. Since the CelerSMS emulator does not support socket commands, this task was completed theoretically using Cavli’s documentation and standard AT command sets.

## Slide 3: About Cavli TCP Modules
Cavli produces IoT modules supporting TCP/UDP communication over cellular networks.
Example module: Cavli C42QM, supporting LTE Cat M1, NB-IoT, and 2G fallback.

## Slide 4: What is Socket Communication?
Socket communication allows direct data transfer between device and server using TCP/IP protocols.
Used for IoT devices to send/receive data over the internet via mobile networks.

## Slide 5: Key Commands used in Cavli Modules
Cavli modules like C42QM use these AT commands for socket operations:
AT+QIOPEN – Opens TCP/UDP socket.
AT+QISEND – Sends data over socket.
AT+QICLOSE – Closes socket connection.

## Slide 6: AT+QIOPEN (Open Socket) Example Command (Cavli C42QM):
AT+QIOPEN=1,0,"TCP","example.com",80,0,1
Opens a TCP connection to example.com on port 80.
Response: OK +QIOPEN: 0,0 (0,0 indicates success).

## Slide 7: AT+QISEND (Send Data)
AT+QISEND=0,50
After prompt, data is entered and sent with Ctrl+Z.
Response: SEND OK
Used to transmit data to the server over the opened TCP connection.

## Slide 8: AT+QICLOSE (Close Connection)
AT+QICLOSE=0
Closes the TCP socket connection.
Recommended after completing data transmission.

## Slide 9: Practical Testing Limitation
CelerSMS emulator does not support TCP socket commands.
Practical testing of these commands must be done on real Cavli modules like C42QM.
This study covers theoretical understanding based on AT command documentation.

## Slide 10: Conclusion
Cavli modules support socket communication via AT commands for IoT applications.
Commands like AT+QIOPEN and AT+QISEND enable direct device-to-server data exchange.
Practical implementation requires physical hardware for full testing.